ADC Module ADC_00

Reads out sets of digital output from sets of ADS7822 12-bit adc chips with output provided as RS232 compliant serial signals. Output may be selected as 1-shot, free-running, pre-set counts, or external trigger. Input is a single-ended analog signal between 0 and Vref. Vref may be set between 0 and +5 Volts.
- Circuit: Trigger(s) from selectable from four sources are used to trigger and enable data conversion from an ADS7822 ADC. A counter, initialized from a signal derived from the triggers, is used to generate 4 pairs of start/stop bits which are superimposed on the readout stream from the ADC. The ADC bits framed by the start and stop bits are then converted to RS232 voltage levels and provided at a serial output.
  - ADS7822
  - RS232
    - UART specific aspects: A variety of documentation suggests that the 16550 series of UART chips process serial data by sampling at 16 times the baud rate. The START bit is detected as an edge while the level of the other bits (data, PARITY, and STOP) are obtained by the middle sample value (8th sampling), sometimes with some protection to ensure that the START bit wasn't spurious.
    - CS, used to enable the ADC, is also used to generate the first START bit by an OR between CS shifted by 1.5 periods and CS shifted by 1 period. The resulting ½ period pulse is used for 2 purposes. It is 1) 're-stretched' to a full period, negative-going pulse delayed by one clock cycle with a shift-register, and 2) it is used to initialize a counter. The 're-stretched' pulse provides the first START bit. The output of the counter is delayed by one clock cycle using the same shift-register used to generate the 're-stretched' pulse, providing the START bits for the 2nd, 3rd, and 4th 8-bit words. The output from the counter is also used to re-initialize itself on completing each count-down cycle. An inverted copy of the counter output is used as the STOP bit for each 8-bit word.
    - Sampling times
    The table below summarizes the center sampling time of each bit in an 8 bit word relative to the leading edge of the START bit (falling edge in TTL, rising edge in RS232), assuming 115.2 kbps baud rate.
Bit 7	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0	Stop Bit
13.0 usec	21.7	30.38	39.06	47.74	56.42	65.1	73.78	82.46

  - Timing.
Several of the chips in the circuit have specific timing requirements that needed to be attended to in order to achieve the appropriate coordination for parsing the 25 bits of ADC output into 8-bit words and inserting start and stop bits. Key points are:
1. 40102 BCD down counter. Uses CK. Transitions are on Low to High edges. As long as CS is asserted, it will reset itself when a countdown is complete.
2. 74LS164 8-bit shift register. These transition at Low to High edges. Some of them use CK and some use CK in the circuit.
3. 74LS74 D-type Flip-flop
4. 74LS76 JK Flip-Flop.
5. NE555 timer (two of these). One implements a monostable to provide CS synchronized to the falling edge of a short pulse which itself is synchronized with the falling edge of CK to make it compatible with the clocking of the ADS7822. With the values provided, CS should be approximately 330 nsec long, ending before a 5th START bit would be sent out but after the 4th START bit. The 4th word contains no valid data so its value is immaterial except possibly for error checking. A second 555 is used in the free-running mode to provide a continuously set of pulses for CT.
6. ADS7822: Bit transitions occur on Falling edge of clock. CK is used as the clock. CS is generated to fall with the falling edge of CK.
  - Readout type selection
    - Each read-out type provides a mechanism for generating pulse, CT. CT is synchronized to rise with CK using a 7474 D-type flip-flop. The flip-flop output is logically OR'd with a slightly delayed and inverted version of itself to generate CM which triggers the CS-generating monostable. The delay is provided by a set of 5 inverters and yields a 15-20 nsec pulse using TTL devices.
    - One-shot: A debounced pushbutton (buffer the switch output with a 7432 filtering the input to ground through a capacitor) with an inverter generates CT.
    - Free-running: An SPDT switch enables an astable implemented with a 555 operating at a frequency appropriate to allow the 4 8-bit reads. The astable output is inverted and the resulting low portion of the waveform provides CT.
    - Preset count – not yet implemented.
    - External Trigger – not yet implemented.
  - Multi-ADC readout
    - Multiple ADCs are read out by sending CS to a set of J/K flip-flops with outputs sent to a decoder (74138). The decoder sends each CS through one of its outputs, each of which is the direct CS used for each respective ADC.
  - Output data
Data is provided as a set of 4 8-bit RS232 words at a fixed 115.2 k bps rate. The ADC provides 25 data bits in MSB to LSB order and then LSB to MSB order. The 4th word consists of logic-0's output by the ADC during the portion that CS is high but after the last data bit has been read and logic-1's from the pullup on the tri-stated ADC output when CS is low. The data bits are fully contained within the first 3 of the 4 8-bit words read out. Bits 2,3, 7, and 8 are read only once as their timing locations for the second time they are read are used for start and stop bits between the 1st and 2nd and between the 2nd and 3rd 8-bit words.
Serial out bit order:
8-bit word	Serial Out 1st bit	Serial Out 2nd bit	Serial Out 3rd bit	Serial Out 4th bit	Serial Out 5th bit	Serial Out 6th bit	Serial Out 7th bit	Serial Out 8
1	11	10	9	8	7	6	5	4
2	1	0	1	2	3	4	5	6
3	9	10	11	LOW	LOW	LOW	LOW	LOW
4	X	HIGH	HIGH	HIGH	HIGH	HIGH	HIGH	HIGH

Readout Software
Basic testing accomplished by following sequence:
1. cat /dev/ttyS0 > read.txt
2. xxd read.txt > dump.txt
3. dump.txt can be read directly or used as input into other code.
Note that by default, xxd yields hex-encoded data that is in reverse bit-order from what is transmitted over the serial line. The ADC7822 is read out with bits 11 to 4 leading off with bit 11. The output from xxd is bit 4 to bit 11, leading off with bit 4.
  - reverse.py: this script parses the dump.txt file from xxd. Bits 1, 4, 5, 6, 9, 10, and 11 are read twice on each read of the ADC. reverse.py checks that these bits are the same value on each read and then calculates the bit count and Vref-based voltage. Output is the mean and standard deviation of the voltages in dump.txt.
  - reverse.c: c-version of the python script, to be done
  - GNUplot: to be done
- Output Bit Ordering:
  - Oscilloscope (with a stop and start bit between each word)
    - Word 0: B11-B10-B9-B8-B7-B6-B5-B4
    - Word 1: B1-B0-B1-B2-B3-B4-B5-B6
    - Word 2: B9-B10-B11-0-0-0-0-0
    - Word 3: X-1-1-1-1-1-1-1
  - xxd order (issued as a line with concatenated pairs of words):
    - Word 0: B4-B5-B6-B7-B8-B9-B10-B11
    - Word 1: B6-B5-B4-B3-B2-B1-B0-B1
    - Word 2: 0-0-0-0-0-B11-B10-B9
    - Word 3: 1-1-1-1-1-1-1-X
  - sport.c order:
    - Word 0: 1-1-1-1-1-1-1-X
    - Word 1: 0-0-0-0-0-B11-B10-B9
    - Word 2: B6-B5-B4-B3-B2-B1-B0-B1
    - Word 3: B4-B5-B6-B7-B8-B9-B10-B11
- Operation
Free-running: readout from /dev/ttyS0 should begin prior to turning on the ADC. The ADC should be turned off before ending the readout.
Notes:
I have observed at least one instance of a spurious set of 8 bits being inserted into the ouput. I don't know where it came from but the value was 0x72=01110010
- Module Hardware
- Looking at top of Perf board,green connectors from left to right with connector edge toward the viewer:
- (RTS, X) (Empty, X) (DataOut to RxD, Ground), (Ground, empty), (LED, LED), (Empty, Blue cable from switch
- DIP-8 at back left has a 1k resistor from pins 1 to 8, ground for pin 2, ground for pin 3, and Vcc for Pin 4