Resistor values for digital section are taken from the specification of the maximum current for the pass transistor and the desired foldback-protected short-circuit current.
R_1 over R_2 = I_{max} over {V_0+V_{BE}} R_{sc} - V_{BE} over {V_0+V_{BE}} newline R_1 over R_2 = {I_{sc} R_{sc}} over V_{BE} -1.0
 For a maximum current of 1.5 A and short-circuit current of 0.5 A, one obtains R1/R2=0.012 and Rsc=0.53 . Selected values for R1 and R2 are 4.7  and 470 .