PPORT00

This device reads one of two 8-bit words each set by a DIP-switch. It requires an external AC input stepped down to 10 V or so, and connection to external filter capacitors. Voltage rectification and regulation are done on board. The device interfaces to a computer parallel port for readout through a DB25 port. EPP Data Read Cycles are used to deliver one of the two 8-bit words. Select of which word
is determined by a preceding EPP Address Read Cycle.

The layout fits on a 3” x 5” prototype board with 0.100” hole spacing. The DB25 is installed using a DB25 to 0.100” breakout board. Currently, this is procured by www.winfordeng.com.

Note that the DB25 shown on the pcb layout is that of a Female so the pins numbering is upside down.